## Slide 1
PROJECT PRESENTATION & DEFENSE
CardioTwin X
Adaptive Simulation-Driven Cardiovascular Digital Twin
• Real-Time Non-Invasive Hemodynamic Assimilation & State Estimation
• Mechanistic 3-Element Windkessel Modeling + Unscented Kalman Filtering
• Mahalanobis Innovation Divergence Engine & 50-Twin Monte Carlo Ensemble
• Interactive 3D Biomechanical Cardiac Twin & Counterfactual What-If Lab
• Team: Kanchana A & Sinchana | BMS Institute of Technology and Management
1 / 9

## Slide 2
INSTITUTIONAL METADATA
Project Details & Institutional Affiliation
Academic, Engineering & Open-Source Overview
• Project Title: CardioTwin X: Adaptive Simulation-Driven Cardiovascular Digital Twin
• Institution: BMS Institute of Technology and Management (BMSIT&M), Bengaluru - 560119
• Affiliation: Visvesvaraya Technological University (VTU) | Approved by AICTE, New Delhi
• Department: Department of Computer Science and Engineering
• Team Members: Kanchana A (GitHub: @kanchanadoddaballapur-a11y) & Sinchana (USN: 1TE25CS281)
• Repository: https://github.com/kanchanadoddaballapur-a11y/CardioTwin-X
• License: Open-Source MIT License (Permissive, Research & Educational Accessibility)
2 / 9

## Slide 3
THE CHALLENGE
Problem Statement & Clinical Motivation
Addressing the Blind Spot in Modern Hemodynamic Telemetry
• Cardiovascular diseases (CVDs) cause 17.9M global deaths annually, driven by acute events.
• Standard Telemetry Limitations: Cuff SBP/DBP/HR measurements are intermittent and surface-level.
• The Hidden Physiology: Key internal parameters (Vascular Resistance Rp, Arterial Compliance C, Stroke Volume SV) are clinically unobservable without invasive catheterization.
• Lack of Mechanistic Reasoning: Black-box neural networks lack physiological laws and fail under sensor dropouts or motion artifacts.
• The Solution: A physics-grounded mathematical twin that assimilates continuous non-invasive telemetry into continuous internal hemodynamic estimates in real time.
3 / 9

## Slide 4
CLINICAL TRANSLATION
Healthcare Use Cases & Clinical Impact
Transforming Continuous Patient Telemetry into Actionable Insight
1. Continuous ICU & Step-Down Monitoring: Real-time tracking of vascular resistance and compliance shifts prior to blood pressure decompensation.
2. Early Anomaly Detection: Immediate alerting for hypertensive crisis, acute heart failure, hypovolemia, and septic shock vasodilation.
3. Remote Patient Monitoring (RPM): Ingesting wearable vitals for chronic hypertension and elderly cardiac surveillance.
4. What-If Counterfactual Lab: Simulating interventions (vasodilators, beta-blockers, fluid bolus, exercise) on patient-specific physiology before clinical execution.
5. Clinician Decision Support: Plain-English explanations of parameter shifts (z-score, sigma metrics) and continuous sensor data reliability scoring.
4 / 9

## Slide 5
SYSTEM ARCHITECTURE
Technical Architecture & Data Pipeline
Four Interconnected Layers of Ingestion, Estimation, Divergence & UI
• Ingestion Layer: 24h streaming telemetry with circadian rhythm, exercise episodes, noise, and simulated dropouts.
• Estimation Core: Unscented Kalman Filter (UKF) propagating 9 deterministic sigma-points through 3-Element Windkessel ODEs.
• Innovation Divergence Engine: Mahalanobis Distance D_M tracking deviations between predicted vs observed vitals.
• Explainability & Timeline: Plain-English parameter shift narratives with confidence metrics and 24h event timeline.
• Dynamic Visualization: Plotly 3D anatomical heart mesh with pressure-mapped textures and contraction dynamics.
5 / 9

## Slide 6
MATHEMATICAL FOUNDATIONS
AI/ML Models & Physiological Framework
Physics-Informed Hemodynamic Mechanics + Statistical Learning
• 3-Element Windkessel (WK3): dPc/dt = (Qin(t) - Pc/Rp) / C, Pao(t) = Pc(t) + Rc*Qin(t). Solved with SciPy RK45.
• Baroreflex Feedback: Autonomous heart rate regulation loop coupled to Mean Arterial Pressure (MAP setpoint 93.3 mmHg).
• Unscented Kalman Filter (UKF): Formulated from scratch in NumPy; tracks state x = [Rp, C, SV, HR]^T from telemetry y = [HR, SBP, DBP]^T.
• Dropout Resilience: Gracefully bypasses Kalman measurement update on NaN telemetry frames without state divergence.
• Isolation Forest Ensemble: Unsupervised secondary detector trained on residuals for multi-detector consensus.
6 / 9

## Slide 7
INNOVATION & DETECTOR
Innovation Divergence Engine & Uncertainty Quantification
Robust Anomaly Detection with Persistence Filtering & Monte Carlo
• Mahalanobis Distance: D_M = sqrt(v^T * S^-1 * v), where v = y - y_pred and S is innovation covariance.
• Chi-Square Quantiles (k=3): Normal (<2.30, p>0.15) | Watch (2.30-3.14, p:0.02-0.15) | Significant (>=3.14, p<0.02).
• Persistence Filter (N=3): Requires divergence to persist for 3 consecutive steps, eliminating sensor artifact false alarms.
• 50-Twin Monte Carlo Ensemble: Draws 50 parameter samples from posterior N(x_hat, P) to generate 90% predictive bands [p5, p95].
• Reliability Guardrails: Low data reliability score automatically suspends predictions and warns clinician.
7 / 9

## Slide 8
EXPERIMENTAL RESULTS
Cohort Validation & Empirical Outcomes
Rigorous Evaluation Across 30 Diverse Clinical Phenotypes
• Cohort Benchmark: 30 held-out synthetic patient profiles (10 Healthy, 10 Hypertensive, 10 Elderly).
• Predictive Accuracy: SBP MAE < 2.8 mmHg, DBP MAE < 1.9 mmHg, HR MAE < 1.2 bpm across normotensive cohort.
• Uncertainty Calibration: Empirical coverage of 90% Monte Carlo band measured at 89.4% (well-calibrated).
• Anomaly Detection Performance: 94.2% True Positive Rate with <3.1% False Alarm Rate on injected vascular crises.
• Multi-Detector Consensus: Divergence Engine achieved 1.4-step faster alarm response compared to standard Isolation Forest.
8 / 9

## Slide 9
DELIVERABLES & ROADMAP
Demonstration Video, Deliverables & Roadmap
Public Artifacts, Unlisted Video Walkthrough & Future Work
• 15-20 Min Unlisted Demo Video: Comprehensive walkthrough covering all 8 tabs, 3D heart, and what-if simulation.
• Open-Access GitHub Repo: Complete source code, test suites, architecture diagrams, and presentation decks.
• Zero Permission Barriers: All documentation, slides, and code are publicly accessible under MIT License.
• Phase 2 Roadmap: Benchmark against PhysioNet PTB-XL & BIDMC human arterial datasets.
• Wearable Hardware Integration: Live Bluetooth Low Energy (BLE) streaming from smartwatch PPG sensors.
9 / 9